## Slide 1
A FIVE-PORT
NoC Router
A first-year-friendly, step-by-step tour of how one flit finds its way across a chip.
ONE ROUTER
FIVE INPUTS
FIVE OUTPUTS
ROUTER
North
East
South
Local
RTL + self-checking simulation
01 / 19

## Slide 2
START HERE
What did we build?
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
2 / 19
One small router
It has five input sides and five output sides. It forwards a flit to the output named inside that flit.
A queue at each input
Each input gets its own FIFO. Incoming flits wait safely instead of getting overwritten.
A fair choice
If two inputs want the same output, round-robin arbitration lets them take turns.
The big idea
Store it -> read its destination -> choose a winner -> send it out
This is one router block, not yet a complete network of many routers.

## Slide 3
BEGINNER VOCABULARY
First, learn six useful words
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
3 / 19
Flit
A small bundle of bits moving through the router. Here it is a complete one-flit packet.
FIFO
A queue: First In, First Out. The oldest flit is served first.
Payload
The useful data being carried, like the contents of a delivery box.
Destination
The output number written in the flit: where the flit should leave.
Arbiter
A fair chooser. It picks one input when several want the same output.
Crossbar
The data switch that connects the selected input to its chosen output.
Input = where it entered. Destination = where it must leave.

## Slide 4
PACKET FORMAT
What is inside a flit?
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
4 / 19
Default width: 48 bits
flit[47:45]
DESTINATION 3 bits
flit[44:0] PAYLOAD (45 bits)
The destination is the envelope label. The payload is what is inside the envelope.
Legal destination numbers
0 Local | 1 North | 2 South | 3 East | 4 West
Illegal destination numbers
5, 6, or 7: the router drops the flit and reports the input.
In this simple version, every flit is a complete one-flit packet.

## Slide 5
ROUTER MAP
Meet the five ports
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
5 / 19
ROUTER
1 NORTH
3 EAST
2 SOUTH
4 WEST
0 = Local (the fifth side, used by the local processor)
Every numbered side has both an input and an output connection.

## Slide 6
READY + VALID
How do two sides agree to transfer?
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
6 / 19
Sender says VALID
"I have a flit. I will keep it stable until you accept it."
Receiver says READY
"I have space. You may send the flit now."
TRANSFER = VALID AND READY at a rising clock edge
Input side: in_valid and in_ready let a flit enter its FIFO.
Output side: out_valid and out_ready let a flit leave the router.
If READY is low, wait. Do not change or lose the flit.

## Slide 7
BIG PICTURE
Follow the data through the blocks
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
7 / 19
1 INPUT
ready/valid
->
2 FIFO
wait in line
->
3 ALLOCATOR
choose route
->
4 CROSSBAR
move the bits
->
5 OUTPUT
ready/valid
A different small SystemVerilog module handles each job.
router_5port.sv is the top-level wiring that joins the modules together.

## Slide 8
THE QUEUE
FIFO: each input has its own waiting line
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
8 / 19
Four storage places (default depth = 4)
slot 0
A - oldest
slot 1
B
slot 2
C
slot 3
empty
read_ptr -> slot 0
write_ptr -> slot 3
Read pointer
Points to the oldest flit. A successful transfer advances it.
Write pointer
Points to the next place for a new flit. It wraps around to slot 0.
FIFO count says how many slots are occupied; full and empty protect the queue.

## Slide 9
INPUT BUFFER
Input buffer: the router's front desk
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
9 / 19
UPSTREAM SENDER
valid + data
->
INPUT FIFO
stores up to 4
->
OLDEST FLIT TO ROUTER
The input FIFO preserves arrival order.
If it fills, in_ready goes low so the sender waits.
The router only removes the head after output acceptance.

## Slide 10
ROUTE SELECTION
Switch allocator: read the label, request an output
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
10 / 19
FIFO head flit
flit[47:45] = 3
->
->
REQUEST EAST
If the label is 0-4, request that output. If it is 5-7, mark the flit invalid.
Request
"Input 0 has a valid flit, and it wants East."
Grant
"East selected input 0. It may use the switch."
The allocator decides who may travel; it does not edit the flit.

## Slide 11
FAIR SHARING
Arbitration: take turns for a busy output
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
11 / 19
Three inputs all want East
INPUT 0
INPUT 2
INPUT 4
EAST ARBITER
->
EAST OUTPUT
Round robin
After serving one input, start the next search after it.
Why?
No single input should hog the output forever.
Each output has its own arbiter, so two different outputs may serve traffic together.

## Slide 12
STABLE TRANSFER
Backpressure: please wait, I am busy
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
12 / 19
Receiver: out_ready = 0
I cannot take the flit yet.
Router: out_valid = 1
I will keep the SAME flit ready.
->
Grant lock
The arbiter remembers which input already owns this stalled output.
No FIFO pop yet
The flit stays at the FIFO head, so it cannot be lost or replaced.
When out_ready becomes 1: the handshake happens, then the FIFO pops.

## Slide 13
MOVING THE FLIT
Crossbar: the data switch
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
13 / 19
INPUT 0 flit A
CROSS BAR
EAST
A grant tells the crossbar which input bits to copy to each output.
The crossbar does not change the destination or payload.
An output can accept one flit each clock when ready stays high.
Only an accepted flit causes its source FIFO to pop.

## Slide 14
RTL HIERARCHY
Top-level router: connect the pieces
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
14 / 19
router_5port.sv
FIFO 0
FIFO 1
FIFO 2
FIFO 3
FIFO 4
5 input_buffer instances (each wraps one FIFO)
switch_allocator = destination decode + 5 arbiters
crossbar = route granted data
The top level mostly connects signals. The smaller modules do the individual jobs.

## Slide 15
ONE FLIT JOURNEY
Worked example: Local input wants East
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
15 / 19
We send payload 203 from input 0 (Local), with destination 3 (East).
{3'd3, 45'd203}
destination | payload
1. SEND
Testbench puts the flit on input 0 and asserts in_valid[0].
2. STORE
At a rising edge with in_ready[0], FIFO 0 stores the flit.
3. DECODE
Allocator reads top bits 011. Decimal 3 means East.
Input says where it arrived. Destination bits say where it must leave.

## Slide 16
ONE FLIT JOURNEY
Worked example: East accepts the flit
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
16 / 19
4. ARBITRATE
East chooses input 0 (if another input also wants East, one waits).
5. SWITCH
Crossbar copies the exact 48 bits to out_flit[3].
6. ACCEPT
out_valid[3] and out_ready[3] meet at a rising edge. FIFO 0 pops.
Expected output: East (3) | Same payload: 203 | No bits changed
Hex example: 48'h6000000000CB (top bits 011, lower payload 203)
The testbench checks all 48 output bits against the expected flit.

## Slide 17
SIMULATION
The testbench is a pretend sender + checker
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
17 / 19
DRIVE
Make a flit and put it on an input. Assert valid and wait for ready.
WAIT
Watch ready/valid at clock edges. The router decides when a transfer happens.
CHECK
Compare the output port and the full flit with the expected result.
Important testbench helpers
send_flit(source, flit)
Behaves like a polite sender: it keeps data valid until an input handshake.
expect_transfer(dest, flit)
Checks output valid, output data, receiver ready, and the transfer edge.
If an expected value is wrong, $fatal prints FAIL and stops the run.

## Slide 18
PASS / FAIL
What did our testbench verify?
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
18 / 19
1
Contention + stable grant
PASS
2
All five routes, including Local -> East
PASS
3
Two separate outputs at once
PASS
4
Backpressure + four-entry FIFO
PASS
5
Invalid destination is dropped/reported
PASS
ALL TESTS PASSED | 15 checked transfers / conditions

## Slide 19
WRAP-UP
Run it yourself, then remember the journey
FIVE-PORT NoC ROUTER | BEGINNER WALKTHROUGH
19 / 19
From the repository folder in PowerShell:
iverilog -g2012 -s router_5port_tb -o router_5port_test rtl\noc_pkg.sv rtl\fifo.sv rtl\input_buffer.sv rtl\round_robin_arbiter.sv rtl\switch_allocator.sv rtl\crossbar.sv rtl\router_5port.sv rtl\router_5port_tb.sv
vvp router_5port_test
Look for ALL TESTS PASSED. A FAIL message identifies the check that stopped.
SENDER -> INPUT FIFO -> DESTINATION DECODE -> ARBITER -> CROSSBAR -> RECEIVER
That is the whole router story: queue it, choose a fair path, and deliver it without changing the flit.